## Slide 1
○ | 의사결정
● | 정보전달
○ | 지시사항
대외비
RESTRICTED
2017.10.07
철도영업본부
해외CS팀
미국 덴버 DTS 전동차 66량
MDS 고장 자료 분석 결과

## Slide 2
▣ 견인 장치
1. 총 고장 41,079건 발생
- 40,884건 : 가선 통과시 발생 (고장 아님)  서버에서 처리 필요
- 151건 : 4007호 FMI 수정 작업 불량
- 20건 : 4047호 시운전 차량 오결
- 24건 : 차량 조사 필요
CODE | Fault NAME | # OF FAIL | Severity (1-4) | POSSIBLE CAUSE | REVIEW RESULT
12 | Over voltage of catenary line (VSOVSM) | 10,118 | 4 | 1) At the time of a section passage. 2) Break down of ACPT. 3) Break Down of HV PT on the Roof. 4) Malfunction of GCU. 5) Failure of Tap Changer(Future Installation). | PHASE GAP 통과 - OK
13 | Low voltage of catenary line (VSLVSM) | 10,118 | 4 |  | 
14 | Over current of Secondary current1 (ISOC1SM) | 10,118 | 2 |  | 
67 | Low Voltage of DC Circuit1 (VDLV1SM) | 10,118 | 4 |  | 
16 | Frequency Irregular of Primary Circuit (FIRSM) | 102 | 4 | 1) At the time of a section passage. 2) Break down of ACPT. 3) Break Down of HV PT on the Roof. 4) Malfunction of GCU. | PHASE GAP 통과 - 왜 상기 고장과 횟수가 다른지?
17 | Waveform Irregular of Primary voltage (VSDDSM) | 310 | 4 |  | 
32 | Over Temperature of Inverter power unit (THDIM) | 151 | 3 | 1) Break down of cooling fin. 2) Lack of cooling air. 3) Break down of blower motors. 4) Malfunction of gate control unit. | 4007-INSULATOR FMI후 CONNECTOR 미체결로 인한 ISOLATED 고장임
35 | Blower Motor Fault (BMFS) | 5 | 3 | 1) Break down of blower motors. 2) Break down of NFB installed in the input side of blowers. | 4018, 4031, 4045 차량 조사 필요
38 | Wheel Slip/Slide detected (WSDM) | 2 | 4 | Discconection of P5-connector of the CIF board in the GCU. | 4009호 조사 필요
41 | Backward Speed Detection (BSDM) | 20 | 3 | 1) Malfunction of GCU. 2) Slippery Track. 3) Unexpected grade level. | 4047 시운전 차량 오결임
47 | Occurrence of slight degree of protection (OPR#) | 11 | 3 | A failure of severity level 2 occured. This bit will be activated when fault in LEVEL2 occurs. The fault level is categorized to the following 3 LEVELs; - LEVEL1 means the faults which are produced by the disturbance factors and cause to the Propulsion fault. In this case, Converter, Inverter and Brake chopper are stopped, but K and VCB are not tripped. - LEVEL2 means slight degree fault of Propulsion converter/inverter, which is called as “OPR”. K is tripped when OPR protection is detected. - LEVEL3 means heavy fault of Propulsion converter/inverter, which is called as “OCR”. VCB is tripped when OCR protection is detected. | 차량 조사 필요 및 업체 문서(HCN-L5772-16 and H30Q373/374/375) 필요
71 | Main Transformer failure (MTRFM) | 6 | 3 | 1) Oil pump failure (MTOMN tripped). 2) Oil flow error. | 4035, 4039, 4054 차량 조사 필요
Notes: 1

## Slide 3
▣ DOOR
1. 총 고장 37,666건 발생
- 전체 고장에 대해 원인 조사 및 대책 수립
CODE | Fault NAME | # OF FAIL | Severity (1-4) | POSSIBLE CAUSE | REVIEW RESULT
0 | Resv | 342 |  |  | 
1 | Zero Speed (+) CL | 234 | 4 | Zero Speed (+) CL Status | 
2 | Zero Speed (-) CL | 248 | 4 | Zero Speed (-) CL Status | 
3 | Open TL Command status | 346 | 4 | Open TL command received. Cleared when doors are fully open or other command is issued | 
4 | Close TL Command Status | 248 | 4 | Closing TL command received. Cleared when doors are fully closed or other command is issued | 
5 | Crew Switch Open Command Status | 185 | 4 | Crew Switch Open Command received. Cleared when doors are open or other command is issued | 
6 | Crew Switch Close Command Status | 305 | 4 | Crew Switch Close Command received. Cleared when doors are closed or other command is issued | 
7 | Passenger Door Enable (+) TL | 254 | 4 | Passenger Door Enable (+) TL input | 
8 | Passenger Door Enable (-) TL | 683 | 4 | Passenger Door Enable (-) TL input | 
9 | Passenger Door Open Pushbutton | 535 | 4 | Passenger Door Open Pushbutton status | 
10 | Spare | 372 |  | None | 
11 | Spare | 374 |  | None | 
12 | Door closed status | 413 | 4 | Door is closed (Panel Sensing switch left and right indicate door closed) | 
13 | Door locked status | 261 | 4 | Door is locked (Solenoid Lock switch right and left indicate door locked) | 
14 | Spare | 624 |  | None | 
15 | Door Summary Relay High Monitoring | 809 | 4 | DSR High monitoring input | 
16 | Door Summary Relay Low Monitoring | 233 | 4 | DSR Low monitoring input | 
17 | Spare | 363 |  | None | 
18 | Spare | 11,937 |  | None | 
19 | Reduced Speed Mode | 4,088 | 4 | The DCU detects condition that requires it to move doors in slow speed. | 
20 | Disable Open Mode | 10,876 | 4 | The DCU detects condition that requires it to refuse the door open command. | 
21 | Disable Close Mode | 3,896 | 4 | The DCU detects condition that requires it to refuse the door close command | 
42 | PSS Mismatch | 40 | 3 | The DCU sets this event when there is a mismatch between left and right Panel sensing Switch signals. Root cause could be PSS not adjusted properly. PSS could fail due to contact damaged, contamination, humidity, mechanical failure, thermal effects, wear. DCU input circuit could fail due to overcurrent. issue can also be with door operator harness or connection of wiring between door operator connector and DCU connector. | 
Notes: 2

## Slide 4
▣ HVAC
1. 총 고장 16,644건 발생
- 16,262건 : AC 614V 미검지 건 차량/로직 검토 필요(전 편성 발생)
- 382건 개별 차량 조사 필요
CODE | Fault NAME | # OF FAIL | Severity (1-4) | POSSIBLE CAUSE | REVIEW RESULT
19 | Compressor #2 high pressure transducer fault | 10 | 1 | Bad sensor, bad connections or damaged TCU. | 4016호 조사 필요
20 | Compressor #2 low pressure transducer fault | 18 | 1 | Bad sensor, bad connections or damaged TCU. | 4034, 4047호 조사 필요
22 | Compressor #2 current out of range | 7 | 1 | Bad sensor, bad connections, tripped overload, excessive measured current or damaged TCU. | 4004호 조사 필요
25 | Auto-resetable overhead over heat temperature switch opens | 10 | 1 | Bad overtemp device, bad connections, excessive overhead heater temperature or damaged TCU. | 4004, 4031, 4033, 4066호 조사 필요
31 | Smoke detector alarm | 4 | 1 | Fire detection or bad connection of smoke detector. | 4018호 조사 필요
33 | Compressor #2 defective | 1 | 1 | Malfunctioning of compressor due to high pressure, low pressure, pressure not changing at start-up or current out of range. | 4025호 조사 필요
34 | Smoke detector status | 4 | 1 | Fire detection or bad connection of smoke detector. | 4018호 조사 필요
37 | Fault to detect open damper | 244 | 1 | No open damper detection when damper not activated | 차량 조사 필요
40 | No 614 Vac when 208 Vac present fault | 16,262 | 1 | 614 Vac breaker open or tripped | 차량 조사 필요
42 | Current detected when no overhead heating | 84 | 1 | SSR failure | 4027, 4028호 차량 조사 필요
Notes: 3

## Slide 5
▣ BRAKE
1. 총 고장 213건 발생
- 68건 : 차량 기지 유치시 CUTOUT COCK조작으로 인한 고장으로 추정  조사후 고장 삭제 필요
- 7종 145건은 차량 조사 필요
CODE | Fault NAME | # OF FAIL | Severity (1-4) | POSSIBLE CAUSE | REVIEW RESULT
9 | A End Brake Cylinder Pressure Cutout Cock | 34 | 2 | Status information of the BCP Cutout Cock switch indication. 1 - Cutout Indication (All Truck BCP to actuators released) 0 - No Cutout Indication | 차량 기지내 이동시 사용으로 추정됨-기능 확인후 종결하여 고장에서 제외 필요
28 | F End Brake Cylinder Pressure Cutout Cock | 28 | 2 |  | 
14 | Brake Control Pressure Cutout Cock | 6 | 2 | Status information of the BCC pressure Cutout Cock switch indication. 1 = Cutout 0 = Normal Operation | 
33 | Friction Brake Control Unit Health | 16 | 2 | Based on the FBCU Application software diagnostics of the FBCU hardware. 1 = Diagnostic Event, 0 = operational need to review the events logged in the FBCU history log for the specific cause. The specific causes or faults are grouped based on bit numbers within the CDT/MDS message. | 4012, 4015, 4022, 4035호 조사 필요
35 | Low Car Battery Input | 2 | 2 | Based on the FBCU Application software input of the battery level. 1 = Diagnostic event 0 = Operational | 4048호 확인 필요
39 | Brake Pipe Operating Module | 90 | 2 | Based on the FBCU Application software diagnostics of service brake cylinder pressure. 1 = Diagnostic Event 0 = operational The specific causes or faults are grouped based on bit numbers within the CDT/MDS message. | 업체 차량(20량) 조사 필요
41 | Electronic Relay Valve F End | 5 | 2 |  | 4034, 4049호 차량 조사 필요
43 | Emergency Variable Load Valve A End | 5 | 2 | Based on the FBCU Application software diagnostics of emergency backup pressure. 1 = Diagnostic Event, 0 = operational | 4020, 4024, 4028호 차량 조사 필요
48 | Air Spring Pressure Out of Range A End | 1 | 3 | Diagnostic information of ASP transducer on BPCU. ASP is between (AW3+5) and (AW0–5) psi at above 10 mph. At zero speed, ASP less than (AW0–10) psi for 10s is an event. 1 = ASP is under/over range 0 = ASP is normal range | 4032호 차량 조사 필요
50 | Main Reservoir Pressure Switch | 26 | 2 | Status information based on the FBCU Application software input signal of this pressure switch. 0 = Main Reservoir Pressure Ok 1 = Main Reservoir pressure low | 8량 차량 조사 필요
Notes: 4

## Slide 6
▣ APU
1. 총 고장 10,245건 발생
- 10,026건 : APSx 4QC STOP 관련하여 업체와 조치 방안 협의 필요(전 편성 발생)
- 5종 219건 차량 조사 필요
CODE | Fault NAME | # OF FAIL | Severity (1-4) | POSSIBLE CAUSE | REVIEW RESULT
0 | APSx AC Ground Fault Error | 54 | 3 | Leakage current(s) detected between chassis ground and one or more of the AC output phases. | 차량 조사 필요
7 | APSx Shop Power Contactor K903 Failure | 7 | 3 | K903 (Shp Pwr) fault (4x < 120s) occurs when K903 FdBk ≠ K903 Drv. | 4065호 차량 조사 필요
8 | APSx DC Ground Fault Error | 126 | 3 | Leakage current(s) detected between chassis ground and one or more of the DC outputs. | 차량(25량) 조사 필요
25 | APSx AC Output CB Q301 Tripped | 8 | 3 | AC single phase output circuit breaker Q301 tripped. | 4034, 4045호 차량 조사 필요
29 | APSx 4QC STOP | 10,026 | 4 | 4QC 'Stop' mode caused by either: - loss of enable signal from CCU or - 4QC sub-system fault. | 업체 조치 방안 협의 필요
70 | APSx Battery Temp. Sensor Failure | 24 | 2 | Battery temperature compensation has been disabled due to temperature sensor circuit failure. | 4014호 조차 필요
Notes: 5

## Slide 7
▣ 방송장치
1. 총 고장 25,364건 발생
- 전체 고장에 대해 업체의 원인 조사 및 대책 수립 필요  고장으로 등록하지 않는 방안 강구 필요
CODE | Fault NAME | # OF FAIL | Severity (1-4) | POSSIBLE CAUSE | REVIEW RESULT
0 | CCP failure. | 6,380 | 2 | 1. Power supply error. 2. Damaged CCP1 control board. 3. Loose connection between CCP and CRA. | 업체 조사 필요
2 | VTX failure. | 124 | 2 | 1. PSA (Power supply of CRA ) error. 2. Damage on VTX board. 3. Damage on VRX board of PID. 4. Loose connection between VTX and VRX of PID. | 업체 조사 필요
3 | VOIP failure. | 1,056 | 2 | 1. PSA (P/S of CRA) error. 2. Damaged PAC board. 3. Damaged AAB assembly board. | 업체 조사 필요
4 | PAC failure. | 1,757 | 2 |  | 
5 | LIC Main Process failure. | 9,012 | 1 | 1. PSA (Power supply of CRA ) error. 2. Damage on LIC board. 3. Loosed connection between CRA and CDT. 4. Damage on CDT | 업체 조사 필요
6 | FDI failure | 328 | 3 | 1. Power supply error. 2. Damage on LEDC board. 3. Damage on LED module. 4. Loose connection of Address signal. 5. Loose connection between FDI1 and COMM. | 업체 조사 필요
7 | SDI1 failure | 290 | 3 |  | 
8 | SDI2 failure | 352 | 3 |  | 
9 | SDI3 failure | 276 | 3 |  | 
10 | SDI4 failure | 353 | 3 |  | 
11 | PII1 failure | 672 | 3 |  | 
12 | PII2 failure | 562 | 3 |  | 
13 | VRX1 failure | 260 | 3 | 1. Power supply error. 2. Damaged VRX board. 3. Damaged LCD panel. 4. Loose connection of Address signal. 5. Loose connection between PID1-1 and COMM. 6.Loose coaxial connection between PID1-1 and COMM. | 업체 조사 필요
14 | VRX2 failure | 324 | 3 |  | 
15 | VRX3 failure | 324 | 3 |  | 
16 | VRX4 failure | 250 | 3 |  | 
17 | VRX5 failure | 244 | 3 |  | 
18 | CRA-Main Application failure | 2,776 | 2 | 1. PSA (P/S of CRA ) error. 2. Damaged CNCS board. 3. Damaged HDD board. 4. O/S error. 5. GPS receiver error. 6. Loose connection between GIA and GPS receiver. | 업체 조사 필요
23 | CRA-FTP Application failure | 24 | 2 |  | 
Notes: 6

## Slide 8
▣ CDT
1. 총 고장 106,335건 발생
- 28종 65,304건은 FT ASSERT, COMM LOSS 등으로 차량 장치와 통신 불량(RESET, 점검 등등)으로 인한 일시적인 고장으로 실재 부품의 고장 혹은 기능 이상이 아니므로 고장으로 등록 곤란
- 잔여 10종 중 하기 사항은 41,031건은 추가 확인/협의 필요
CODE | Fault NAME | # OF FAIL | Severity (1-4) | POSSIBLE CAUSE | REVIEW RESULT
0 | Power On or Reset | 2,477 | 4 | Set momentarily each time CDT powers on. Can be used in CDT log to record startup. | 차량 POWER ON시마다 발생하는 것으로 고장아님
1 | Watchdog Reset | 5 | 3 | CDT reset due to watchdog timeout. Possible CDT software or hardware error. | 4065호 차량 확인 요
2 |  | 14 |  |  | 
4 | Power fault: Shutdown | 2 | 2 | CDT power supply shut down due to high temperature, low output voltage or high output current. | 4053호 차량 확인 요
5 | Power fault: High Temp Shutdown | 16,794 | 2 | CDT power supply shut down due to high temperature. | 고장 현상에 대해 업체와 확인 요(전편성 발생함)
9 |  | 16 |  |  | 
13 | Display On | 1,091 | 4 | CDT display is turned on. | 고장 현상에 대해 업체와 확인 요(전편성 발생함)
30 |  | 10 |  |  | 
34 | General Fault trainline Asserted | 683 | 4 | Passenger Door Enable (-) TL input | 고장아님(삭제요)
120 | Neuron Reset | 1,368 | 3 | CDT LonWorks network Neuron has reset. | 하부 장치와 통신 불량시 발생하는 것으로 실재 통신 불량보다는 각 장치의 RESET 등 기타 사항으로 발생하는 것으로 고장 처리는 불가함
Notes: 7