## Slide 1
▣ Communication System Failure (DENVER DTS 66cars) |  | 
◈ Details - Woojin engineer has investigated the fault event log data from 29th May to 16th June. The communication system in saloon is not operated periodically due to GPS data failure. (Normal operation after restarting the device) ◈ Cause 1) Confirm that wrong position value is received from GPS data received through the network switch. 2) When GPS data is received through the network switch, the CNCS is overloaded due to the data proliferation by an unknown reason. ◈ Occurrence - Period: 2017.05~06 (About 20 events / 33 trains) ◈ Responsibility (Company) : - | ◈ temporary measure - Restart the devices when CNCS is overloaded (Network data proliferation occurs) ◈ Action Plan - Woojin engineer is planning to have on-site analysis that the GPS data abnormality input to the communication system using the network analysis tool (Wireshark) after capturing the input/output data from Network switch. ⇒ Plan: 6/30~7/12 (The plan is subject to change according to the program modification) | 
 | Apply to entire trains (Plan) | -
 | - Registration and reflection to the train fault history for (Prevention of similar failure recurrence) | 
Issue
Corrective action
Recurrence prevention Plan
S/W, H/W, Process, Circuit, Component, Etc.
(17.06.23) / Countermeasures in progress
Written
Approved
PTC
GPS
MOXA
*CRA(Communication Rack A)
CNCS
CPU
AMP
PTC
MOXA
CNCS
CPU
AMP
The communication system performance
deteriorates and incapacity occurred
when data proliferation
PTC
GPS
MOXA
PTC
MOXA
data capture(2)
data capture (1)
Network data collecting and check
CRA
CRA