## Slide 1
Woojin’s Scope of Supply for wayside
자동 방송에 대한 공급 범위
- Woojin’s scope of supply for Wayside are the on-board communications system and the software which edits the schedule data needed for operating.
(Supplies the scope colored with yellow.)
WOOJIN
OCC 공급 범위
- 자동 방송을 위한 GPS DATA
- 덴버 시행청은 자동 방송을 위해 필요한 GPS 데이터를 누가 제공 하는지 우진에게 알려 주어야 한다.

## Slide 2
OCC 공급 범위
MDS DATA를 보관할 서버.
MDS 파일을 관리 프로그램
-> SEPTA에서는 시행청이 지정한 업체에서 제작 하였다.
CMU
MDS
Woojin’s Scope of Supply for wayside MDS DATA 관리에 대한 공급 범위
- Woojin’s scope of supply for Wayside are the on-board communications system. (Supplies the scope colored with yellow.)
- 덴버 시행청은 MDS 파일을 보관할 OCC 서버를 누가 공급 하는지 정해야 한다.
- 덴버 시행청은 OCC 서버에서 MDS 파일을 관리할 응용 프로 그램을 누가 제작 할지 정해야 한다.

## Slide 3
Content
관리 S/W
OCC 공급 범위
Content DATA를 보관할 서버.
CMU
Woojin’s Scope of Supply for wayside
Content DATA에 대한 공급 범위
- Woojin’s scope of supply for Wayside are the on-board communications system.
- 우진은 OCC 서버에서 Content 파일을 관리할 응용 프로그램을 제공 한다.
(Supplies the scope colored with yellow.)
- 덴버 시행청은 MDS 파일을 보관할 OCC 서버를 누가 공급 하는지 정해야 한다.

## Slide 4
PUSH BUTTON
- Press PUSH BUTTON Switch with left hand.
- Speaker Select switch will be automatically selected. (No need to select switch)
- Speaker will output when the operator talks.
** Speaker Select Criteria
- Remembers the final status of use.
- Press the Push Button switch and select the switch with right hand if trying to change the direction of the speaker output.
Gooseneck Use Order
Method proposal for Operator using the Gooseneck microphone with his left hand

## Slide 6
- Hold the Handset Microphone with right hand.
- Press the PTT Switch.
- Speaker Select switch will be automatically selected. (No need to select switch)
- Speaker will output when the operator talks.
** Speaker Select Criteria
- Remembers the final status of use.
- Press the PTT switch and select the switch with left hand if trying to change the direction of the speaker output.
DPO Use order
③
①
②
Operation procedure for driver to use DPO microphone

## Slide 7
①
②
①
②
③

## Slide 8
IC Identification Request
Item | Typ | Qty | Part Name | Value | TEMP | STORAGE
WLR | IC | 1 | RTL8309SB, | RTL8309SB(RTL8309SC) | 0~+70 | -55~+150
VOIP | IC | 1 | AC494, BGA | AC494 | 0~+70 | -65~+150
LIC | IC | 1 | W5100 | W5100 | 0~+80 | -55~+120
SSD | MEMORY | 1 | OWC | OWC 120G | 0~ +70 | -55 ~ +150
CPU | CPU | 1 | CONGA-X945/ | CONGA-X945/ | 0 ~ +60 | -20 ~ +80
- These contents are included in the IC temperature list which we submitted during the FDR meeting.
- All PCB IC meets the temperature specification of -20 ℃.
However, we would like Denver to identify above 5 ICs.
- These 5 ICs are necessary for realizing the function and we have also received the approval from SEPTA project.

## Slide 9
Woojin’s product will use Tyco Electronics cable for the equipment internal wiring.
We would like Denver to use following information as references.
Use for Power : 100G1121-0.75-– 0/9
Use for Communication : 100G1121 – 0.5 – 0/9
Use for Voice : 100G1141 – 0.5 – 0/2/6/9
Etc. : 100G0111 – 0.5 - o
Equipment Interior Cable Specification