## Slide 1
MDS Interface 내용 정리
2012. 01. 30

## Slide 2
MDS Interface.

## Slide 3
추가 견적 내용 정리.
LIC 기능 추가.
-> MDS와 Interface 추가.
MDS 위치 정보 전달 로직 추가.
-> CRA – CRA간 차량 정보 전달 로직에 CI 고장 로직 추가.
-> 각 차량 위치 확인 및 고장 정보 전달 로직 추가.
CCP 화면 구성 추가.
-> 차량 정보 전달 상태를 확인 할 수 있는 UI 추가.

## Slide 4
Denver Eagle EMU Project
      - CCP 를 통한 데이터 입력 방식 및 피드백 방법 – 1.
      Lonworks Network
      Lonworks Network
      RS 485
      CCP (Comm. Control Panel)
      MDS (CDT)
      Converter/Inverter
      Information for car network
      (1) Train configuration info.(2 bits)
      00 ; 2-cars
      01 ; 4-cars
      10 ; 6-cars
      11 ; 8-cars
      (2) C/I position (8 bits = bit 3-10)
      10000000 ; no. 1 car
      CRA
      (Comm. Rack A)
CI-SDR
CI-SDR
CI-SDR
CRA-SD
CRA-SD
CRA-SD
Input Data
피드백 Data
CCP에서 입력된 Data를 CRA는 485 통신 방식으로 입력을 확인 한다.
CRA는 Ci로 Lonworks Net work를 이용하여 Data를 전달 한다.
Ci는 수신한 데이터를 CRA로 Lonworks Networks를 이용하여 피드백 한다.
CRA는 Ci로 부터 받은 피드백 Data를 485 통신 방식으로 CCP로 전달 한다.
SDR : Send Data Request
SD : Send Data

## Slide 5
      Lonworks Network
      Lonworks Network
      RS 485
      CCP (Comm. Control Panel)
      MDS (CDT)
      Converter/Inverter
      CRA
      (Comm. Rack A)
CI-SDR
CI-SDR
CI-SDR
CRA-SD
CRA-SD
CRA-SD
피드백 Data
CRA는 각 차량에 구성 정보를 수집하고, 각 차량의 열차 번호를 이용하여 차량 번호가 낮은 순서 부터 순차적으로 위치정보를 부여 한다.
CRA는 Ci로 Lonworks Net work를 이용하여 Data를 전달 한다.
Ci는 수신한 데이터를 CRA로 Lonworks Networks를 이용하여 피드백 한다.
CRA는 Ci로 부터 받은 피드백 Data를 485 통신 방식으로 CCP로 전달 한다.
SDR : Send Data Request
SD : Send Data
      - CCP 를 통한 데이터 입력 방식 및 피드백 방법 – 2.
      CRA
      (Comm. Rack A)
차량 구성 정보를 이용하여 CI 위상 제어 정보를 자동으로 전달 한다.
(차량 번호를 이용하여 차량 번호가 낮은 순서대로 차례대로 순서를 설정 한다.)
Denver Eagle EMU Project

## Slide 6
      RS 485
      CCP (Comm. Control Panel)
      CRA
      (Comm. Rack A)
      RS 485
      CCP (Comm. Control Panel)
      CRA
      (Comm. Rack A)
      RS 485
      CCP (Comm. Control Panel)
      CRA
      (Comm. Rack A)
      RS 485
      CCP (Comm. Control Panel)
      CRA
      (Comm. Rack A)
      Phase Shift (degree)
135
45
90
0
120
60
X
0
      Lonworks Network
      Lonworks Network
      MDS (CDT)
      Converter/Inverter
Excessive Noise
Fault
Data
Fault
Data
Fault
Data
Fault
Data
Fault
Data
CI 고장 정보를 다른 차량에 전송한다.
전체 차량 고장 정보 전달에 최대 90초가 걸린다.
      Phase Shift _ 8-cars
      CRA(PA) – MDS – Converter/Inverter, (8) When a Converter/Inverter is Failed
      - CI 고장 정보를 다른 차량에 전달 하는데 MAX 90초가 소요된다.
Denver Eagle EMU Project

## Slide 7
      Phase Shift _ 2-cars
      - CRA(PA) – MDS – Converter/Inverter, (1) when START UP
Denver Eagle EMU Project
      Phase Shift (degree)
--
--
--
--
--
--
90
0
      RS 485
      Lonworks Network
      Lonworks Network
      Lonworks Network
      Lonworks Network
      RS 485
      CCP (Comm. Control Panel)
      MDS (CDT)
      Converter/Inverter
      MDS (CDT)
      Converter/Inverter
      CCP (Comm. Control Panel)
      RS-485
      Information for car network
      (1) Train configuration info.(2 bits)
      00 ; 2-cars
      01 ; 4-cars
      10 ; 6-cars
      11 ; 8-cars
      (2) C/I position (8 bits = bit 3-10)
      10000000 ; no. 1 car
      CRA MB
      (Comm. Rack A)
      CRA MA
      (Comm. Rack A)
      RS-485
CI-SDR
CI-SDR
CI-SDR
CRA-SD
CRA-SD
CRA-SD
피드백 Data
CI-SDR
CI-SDR
CI-SDR
CRA-SD
CRA-SD
CRA-SD
Input Data
피드백 Data

## Slide 8
      Phase Shift _ 2-cars
      - CRA(PA) – MDS – Converter/Inverter, (2) When a Converter/Inverter is Failed
      Phase Shift (degree)
--
--
--
--
--
--
90
X
Excessive Noise
      Information for car network
      Failure of Converter/Inverter
      10000000 ; no. 1 car fault
      RS 485
      Lonworks Network
      Lonworks Network
      Lonworks Network
      Lonworks Network
      RS 485
      CCP (Comm. Control Panel)
      MDS (CDT)
      Converter/Inverter
      MDS (CDT)
      Converter/Inverter
      RS-485
      CRA
      (Comm. Rack A)
      CRA
      (Comm. Rack A)
      RS-485
FAILURE
Denver Eagle EMU Project

## Slide 9
      Phase Shift _ 4-cars
      - CRA(PA) – MDS – Converter/Inverter, (3) when START UP
      Phase Shift (degree)
--
--
--
--
135
45
90
0
      RS 485
      RS-485
      Lonworks Network
      Lonworks Network
      Lonworks Network
      Lonworks Network
      RS 485
      RS-485
      CCP (Comm. Control Panel)
      MDS (CDT)
      Converter/Inverter
      MDS (CDT)
      Converter/Inverter
      CCP (Comm. Control Panel)
      RS-485
      Information for car network
      (1) Train configuration info.(2 bits)
      00 ; 2-cars
      01 ; 4-cars
      10 ; 6-cars
      11 ; 8-cars
      (2) C/I position (8 bits = bit 3-10)
      00100000 ; no. 3 car
      CRA
      (Comm. Rack A)
      CRA
      (Comm. Rack A)
      RS-485
Denver Eagle EMU Project

## Slide 10
      CCP (Comm. Control Panel)
      Phase Shift _ 4-cars
      - CRA(PA) – MDS – Converter/Inverter, (4) When a Converter/Inverter is Failed
      Phase Shift (degree)
--
--
--
--
120
X
60
0
      Information for car network
      Failure of Converter/Inverter
      00100000 ; no. 3 car fault
      RS-485
      Lonworks Network
      Lonworks Network
      Lonworks Network
      Lonworks Network
      RS-485
      CCP (Comm. Control Panel)
      MDS (CDT)
      Converter/Inverter
      MDS (CDT)
      Converter/Inverter
      RS-485
      CRA
      (Comm. Rack A)
      CRA
      (Comm. Rack A)
      RS-485
      RS 485
      RS 485
Denver Eagle EMU Project

## Slide 11
      Phase Shift _ 6-cars
      - CRA(PA) – MDS – Converter/Inverter, (5) when START UP
      Phase Shift (degree)
--
--
90
0
135
90
45
0
      RS-485
      Lonworks Network
      Lonworks Network
      Lonworks Network
      Lonworks Network
      RS-485
      CCP (Comm. Control Panel)
      MDS (CDT)
      Converter/Inverter
      MDS (CDT)
      Converter/Inverter
      CCP (Comm. Control Panel)
      RS-485
      Information for car network
      (1) Train configuration info.(2 bits)
      00 ; 2-cars
      01 ; 4-cars
      10 ; 6-cars
      11 ; 8-cars
      (2) C/I position (8 bits = bit 3-10)
      00100000 ; no. 3 car
      CRA
      (Comm. Rack A)
      CRA
      (Comm. Rack A)
      RS-485
      RS 485
      RS 485
Denver Eagle EMU Project

## Slide 12
      Phase Shift _ 6-cars
      - CRA(PA) – MDS – Converter/Inverter, (6) When a Converter/Inverter is Failed
      Phase Shift (degree)
--
--
90
0
120
X
60
0
      CCP (Comm. Control Panel)
      Information for car network
      Failure of Converter/Inverter
      00100000 ; no. 3 car fault
      RS-485
      Lonworks Network
      Lonworks Network
      Lonworks Network
      Lonworks Network
      RS-485
      CCP (Comm. Control Panel)
      MDS (CDT)
      Converter/Inverter
      MDS (CDT)
      Converter/Inverter
      RS-485
      CRA
      (Comm. Rack A)
      CRA
      (Comm. Rack A)
      RS-485
      RS 485
      RS 485
Denver Eagle EMU Project

## Slide 13
      Phase Shift _ 8-cars
      - CRA(PA) – MDS – Converter/Inverter, (7) when START UP
      Phase Shift (degree)
135
45
90
0
135
45
90
0
      RS-485
      Lonworks Network
      Lonworks Network
      Lonworks Network
      Lonworks Network
      RS-485
      CCP (Comm. Control Panel)
      MDS (CDT)
      Converter/Inverter
      MDS (CDT)
      Converter/Inverter
      CCP (Comm. Control Panel)
      RS-485
      Information for car network
      (1) Train configuration info.(2 bits)
      00 ; 2-cars
      01 ; 4-cars
      10 ; 6-cars
      11 ; 8-cars
      (2) C/I position (8 bits = bit 3-10)
      00100000 ; no. 3 car
      CRA
      (Comm. Rack A)
      CRA
      (Comm. Rack A)
      RS-485
      RS 485
      RS 485
Denver Eagle EMU Project

## Slide 14
      Phase Shift _ 8-cars
      - CRA(PA) – MDS – Converter/Inverter, (8) When a Converter/Inverter is Failed
      Phase Shift (degree)
135
45
90
0
120
X
60
0
      CCP (Comm. Control Panel)
      Information for car network
      Failure of Converter/Inverter
      00100000 ; no. 3 car fault
      RS-485
      Lonworks Network
      Lonworks Network
      Lonworks Network
      Lonworks Network
      RS-485
      CCP (Comm. Control Panel)
      MDS (CDT)
      Converter/Inverter
      MDS (CDT)
      Converter/Inverter
      RS-485
      CRA
      (Comm. Rack A)
      CRA
      (Comm. Rack A)
      RS-485
      RS 485
      RS 485
Denver Eagle EMU Project